## Slide 1: SHREE SWAMI ATMANAND SARASVATI INSTITUTE OF TECNOLOGY

## Slide 2: PRESENTED BY: 1.PATEL FENIL A. 2.PATEL KHUSHI 3.PATEL PURVI M. 4.PORIYA JAYESH M. 5.PRAJAPATI HARSH D.

## Slide 3: CONTENTS:
Introduction of ultrasonic
Properties of ultrasonic wave
Production of ultrasonic wave

## Slide 4: Introduction of ultrasonic
The frequency of ultrasonic wave is greater then 20KHz.
Their wave length are small.
They can travel over long distance as a highly directional beam.
They have high energy content.
Their speed of propagation increase with increase in frequency.

## Slide 5: Production of ultrasonic waves
Based on frequency range and power output, the ultrasonic wave generation are divided into two groups.
The electrical generators are subdivided into two categories.
(i) Magnetostriction generator or oscillator
(ii)piezoelectic generator or oscillator

## Slide 6: Magnetostriction method
When a ferromagnetic material in the form of a rod is subjected to an alternating magnetic field parallel to its length to its length as shown in figure, the rod undergoes alternate contraction and expansions at a frequency equal to the frequency of the applied magnetic field.

## Slide 7: Construction
The ferromagnetic rod AB is clamped at the middle x. the coil L1and L2 are would at the end of the rod. To the coil L1a variable capacitor C1 is connected in parallel and this combination form the tank or resonant circuit. One side of the resonant circuit is connected to the collector of the transistor through a milliammeter. The other side of the resonant circuit is connected to the emitter through a battery . The coil L2 is connected between the base and the emitter and is used as a feed a back loop.

## Slide 8: Working
When the battery is switched on, the resonant circuit L1C1 in the collector circuit of the transistor sets up an alternating current of frequency,
f = 1 / (2π √L C)
As a result, the rod gets the Magnetised by the collector. Any change in collector current brings about the changes in the Magnetisation, and consequently a change in the length of the rod.

## Slide 9: The frequency of ultrasonic waves produced by this method depend upon the length l, density p, and elastic constant E of the rod. i.e., thus by varying l and E of the rod, ultrasonic waves can be generated at any desired frequency. Hence, at resonance condition,

## Slide 10: Merits:- 1. The design of this oscillator is very simple and production cost is low. 2. At low ultrasonic frequencies, large power output is possible without the risk of damage to the oscillator circuit. 3. Frequencies ranging from 100KHz to 3000KHz can be produced. Demerits:- 1. It can’t generate ultrasonic of frequency above 3000KHz. 2. The frequency of oscillator depends greatly on temperature.

## Slide 11
PIEZOELECTRIC METHOD

## Slide 12
PIEZO ELECTRIC METHOD
Piezo electric effect:
If one pair of opposite face of a crystal is subjected to pressure, the other pair of opposite faces develops electric charge.
PRINCIPLE
Inverse Piezo electric effect:
If the alternating voltage is applied to one pair of faces, the opposite faces expands and contracts periodically thereby generating elastic waves.
Example: Quartz, tourmaline and Rochelle salt

## Slide 14
Construction
At Resonance,
frequency of oscillation in the tank circuit
= natural frequency of vibration of the crystal
where P = 1,2,3,4 … etc. for fundamental, first over tone, second over tone etc.,

## Slide 15
Advantages
Ultrasonic frequencies as high as 500 MHz can be obtained
Output of this oscillator is very high.
Not affected by temperature and humidity.
Disadvantages
Cost of Piezo electric quartz is very high.
Cutting and shaping of quartz crystal are very complex.

## Slide 16: ULTRASONICS

## Slide 17: ULTRASONIC IN IDENTIFYING DEFECTS
It is based on the principle of sending out ultrasonic beam into a yest specimen and by analysing the reflected beam from the flaws,the presence and location of flaws are studied.
The defects may be classified into two groups .
Those Occuring at the Surface
These include cracks resulting from unsatisfactory conditions during cooling of the casting ,cracks produced duringvheat treatment processes,surfase scale and defects due to the rolling in of laps or scabs and seams.
2. Those Occuring Below the Surface
These include porosity,lamination,inclusions of various types,segregation blow holes,internal cracks and other less abvious faults such as coarse grain.

## Slide 18: Basic Equipments Used in Ultrasonic Methods
An electronic signal generator to generte alternating voltage when electronically triggered.
A sending transducetr that emits abeam of ultrasonic waves when alternating voltages are applied to it.
A receiving transducer to accept the output of ultrasonic wave from the test specimen and convert it to an electric signal.
An electronic device to smplify and modify the signal from the receiving transducer and project it on a display device (CRO).
An electronic clock or timer to measure the minute time interval between the sending and receiving of the signal.

## Slide 19: PULSE ECHO SYSTEM
The Pulse Echo system is the widely used ultrasonic test.
In this system ,a single transducer is used for both sending and receiving the ultrasonic sound waves,as shown in figure.

## Slide 20
In the pulse echo system evenly timed pulses of ultrasonic sound waves are produced from a pulse generator which are transmitted into the material being tested.
As the waves pass through the top surface of the material being tested,there will be a pattern or ‘pip’ on the oscilloscope screen labelled A,and if there is no defect in the specimen the ‘pip’ of reflected pulse will appear at ‘C’ as shown in figure.

## Slide 21
If the test specimen has a flaw within it, the wave will get reflected back and smaller ‘pip’ ofwill appear on the entire thickness as indicated by the letter C in figure.
The reflected pulse from the flaw will appear as a smaller ‘pip’ between the other two , i.e.,one from top and the other from bottom.Scince the distance between the pips on screen represnts elapsed time of the reflected pulse,the distance to a flaw can be accurately measured.

## Slide 22: ULTRASONIC FLAW DETECTOR
The through yransmission system requires the use of two transdusers,one for transmitting or sending the sound waves,and the other for receiving the sound waves,as shown in figure.

## Slide 23
The pulse of ultrasonic waves are transmitted into and through the material.
The transmitted ultrasonic wavez get reflected When they encounter a crack or cavities in the interior of the metal block.
The reflected pulse is received by the receiving transducer in the form of a sound wave and converted into an electrical signal and fed to the CRO screen through an amplifier,and the time t taken to come back is noted.
If the velocity v of thecultrasonic waves in that metal is known ,the position d of the crack can be located(d=vt).The exact size and shape of the cavity or crack can be found out by examining the metal specimen from all directions.

## Slide 24: Advantages of Ultrasonic Inspection Method
It is more accuratethan radiography method.
It is very cheap and it has a high speed of operation.
Large size specimen can be inspected in a very short duration .
Deep-seated defects minute flaws can also be detected.
Location,nature and size of a defect can be accurateky determined.
It is used to detect the flaws in all common structured metals,non-metals and other materials like rubber types etc.

## Slide 25: Limitations
No permanent record of the flaw can be obtained and it can be observed obly on the screen.
Only skilled and well- trained technicians can perform this testing.
That are rough,irregular in shape ,very small ar thin or not homogeneous are difficult to inspect.
Discontinuities that are present in shallow layers immeditely beneath the surface may nat be detectable.

## Slide 26: SHREE SWAMI ATMANAND SARASVATI INSTITUTE OF TECHNOLOGY
Subject :Physics
Topic: : Ultrasonic Waves & NDT
Subject code: 2110011
Branch: CIVIL 01
Prepared by: Patel Purvi M.

## Slide 27: Content:
What is Non-destructive Testing?
Comparison of destructive and non-destructive tests.
Ultrasonics in identifying Defects

## Slide 28: What is Non-destructive Testing?
NDT is defined as the process of testing the material without causing any damage or reducing the service life of the component.
After the test process is over, the material can be used again for the same purpose for which it was made.
It is used to locate the defects or flawsin the component.

## Slide 29
The general objectives of NDT may be classified as follows:
To Increase Serviceability
Here NDT is used to detect faults which are likely to reduce the service-life of the finished components.
For example, some defect, whether occurring at the surface or below the surface can initiate fatigue failure.
If these defects are detected at an early stage, the service-life of the components or materials can be increased.

## Slide 30
b) To Improve Productivity and to Increase the Profits
Defective materials has to be located at an early stage in production so that further manpower is not frustrated in futile processing.
There is less useless wear and tear on plant.
These are obvious advantages of testing at an early stage of basic work pieces, such as castings and welds.
Hence, testing a component at an early stage of production itself increases quality of product and, in turn, the profits also.

## Slide 31
Destructive Tests
Non-destructive Tests
Measurement are direct and reliable.
Test are not made on the object directly.
Time consumption is genetrally high.
In service testing is not possible.
Preparation of the test specimen is costly.
Measurement are indirect and reliability has to be verified.
Test are made directly on the object .
100% testing on the actual component is possible.
Usally qualitative measurement.but, qualitative measurement can also be done.
In service testing is possible.
Very little preparation is sufficient.

## Slide 32: SHREE SWAMI ATMANAND SAEASVATI INSTITUTE OF TECHNOLOGY
Subject : physics
Topic : Ultrasonic Waves & NDT
Subject code : 2110011
Branch: CIVIL 01
PREPARED BY : PORIYA JAYESH M.
ENROLLMENT NO. 190760106040

## Slide 33: CONTENT :
PULSE ECHO SYSTEM
ULRASONIC FLAW DETECTOR (THROUGH TRANSMISSION SYSTEM )
ADVANTAGE OF ULRASONIC INSPECTION METHOD
LIMITATIONS

## Slide 34: Pulse echo System
The pulse echo system is the most widely used ultrasonic test . In this system ,a single transducer is used for both sending and receiving the ultrasonic sound waves, as shown in figure 4.10 .
For a better contect of the transducer with the metal surface couplets like thin oil or glycerine is used
In the pulse echo system evenly timed pulses of ultrasonic sound waves are produced from a pulse generator which are transmitted into the material being tested .
As the waves pass through the top surface of the material being tested,there will be a pattern or ‘pip’ on the oscilloscope screen labelled A ,and if there is no defect in the sprcimen the ‘pip’ of reflected pulse will appear at ‘c’ . As shown figure 4.10 (a)

## Slide 36
If the test specimen has as flaw within it, the wave will get reflected back and a smaller ‘pip’ will appear on the screen labelled as B , as shown in figure 4.10(B) the specimen is also tested through it is entire thickness as indicated by the letter C in figure 4.10 (b)

## Slide 38
The reflected pulse from the flaw will appear as a smaller ‘pip’
between the other two , i.e . One from top and other from bottom since the distance between the tips on the oscilloscope screen repercted elapsed time of the reflcted pulse , the distance to a flow can be accurately measured

## Slide 39: Ulrasonic flaw detector (thrugh transmission system)
The through transmission system requires the use of two transducers . One for transmitting or sending the sound waves , and the other for receiving the sound waves , as shown in figure 4.11
The pulse of ultrasonic waves are transmitted into and through the material
The transmitted ultrasonic waves get reflected when they encounter a creck or cavities in the enterior of metal block the reflcted pulse receivied by the receving transducer in the from of sound waves and convrected into an electrical signal fed to the CRO screen through an amplifier and the time taken to come back is noted

## Slide 40
if the velocity v of the ultrasonic waves in the metal is known , the position d of the crack can b located the exact size and shape of the cavity or crack can found out by examining the metal specimen from all directions .

## Slide 41: Advantages of ultrasonic inspection method
It is more accurate than radiography method.
it is very cheap and it has a high speed of operation .
Large size specimen can be inspected in a very short duration .
Deep seated defects and size of a defect can also be detected .
Location , nature and size of a defect can be accurately determined .

## Slide 42: Limitations
No permanted record of the flaw can be obtained and it can be observed only on the screen .
Only skilled and well trained technicians can perform this testing .
Parts that are rough , irregular in shape , very small or thin or not homogenrous are difficult to inspect.
Discontinuities that are present in shallow layers immediately beneath the surface may not be detectable.